## Slide 1: Wideband Rx
Lineup and System Specs + Base Band LPF

## Slide 2: Recap: Proposed Line-up
Cascade analysis (Max gain)

## Slide 3: Recap: Proposed Line-up
Cascade analysis (Min. gain)

## Slide 4: Recap: Simulation setup
Matlab simulation uses memory-less non-linear model for RF Blocks: Vo= α1 Vin + α2 Vin 2 + α3 Vin 3
RF blocks are cascaded as follows:
              Vo_(n+1) = α1Vo_n + α2Vo_n 2 + α3Vo_n 3
For noise calculation , Friis’ equation is used.
Problem setup: RF BW = 400MHz , LO frequency = 1GHz, RF tone1 = 1.17GHz, RF tone2 = 1.18GHz
CW blocker: Power = -15dBm , at 1.3GHz
Blocker appears at Psens + 6dB

## Slide 5: Recap: Simulation setup (Cont.)
DC offset is assumed to be canceled completely
Baseband Filter Specs:
Rejection at 300MHz = 25dB
OIP2 = 55dB (for filter and VGA)
Maximum peak power for ADC = -10dBm
Assuming PAR = 10dB → Maximum average power = -20dBm
ADC integrated noise power (200MHz ) = -66dBm → Enob = 9bits

## Slide 6: Two tone test – output spectrum
Input power (two tones) = -50dBm (Note that this is actually double sided spectrum and BlackmanHarris window is used for FTT to reduce FTT noise floor)

## Slide 7: SNR, SDR and SNDR without blockers

## Slide 8: SNR, SDR and SNDR (With blocker and IP2)

## Slide 9: Maximum Input power for ADC

## Slide 10: Gain Policy Under Blocking : First DSA

## Slide 11: Gain Policy Under Blocking : Second DSA

## Slide 12: Gain Policy Under Blocking: VGA

## Slide 13: Gain Policy Under Blocking: Total Gain

## Slide 14: Wideband Rx
Baseband LPF schematic

## Slide 15: Baseband LPF specs:
First Mode:
Rejection at 300MHz = 25dB (changed later to 30dB)
0.5dB BW = 250MHz
OIP3 = 16dBm
NF = 12dB
Gain = 0dB
Second Mode : 3dB BW = 600MHz , 0.5dB BW = 250MHz

## Slide 16: Filter Approximation:
5th order Elliptic Approximation is used:

## Slide 17: Filter Approximation: topology selection
Poles Quality factors:
8.9, 1.5, 0.5(real pole)
Since maximum Q > 4 Bi-quad doesn’t have good
component sensitivity for high Q→ use LC ladder simulation instead
Leap-frog implementation is used
GM-C implementation is chosen for high BW

## Slide 18: Filter Behavioral Modeling:
Note: Actual filter is differential , this is just a behavior model for SLICAP simulation

## Slide 19: Lossy integrator:
Doing some iterations required GM-cell gain can’t be less than 200 → AV is chosen to be 250
Losses Mapping is required to determine C/gm.
Losses mapping is done with SLICAP

## Slide 20: Losses Mapping
With losses mapping
Without losses mapping

## Slide 21: Losses Mapping (Normalized PZ-map)
With losses mapping
Without losses mapping

## Slide 22: Losses Mapping (pole-zero map)
It appears that solver struggles with mapping zeros that’s because these zeros is lossless ,for this reason losses mapping doesn’t improve the response so much.

## Slide 23: More Optimized Response:

## Slide 24: Required C/gm:
C₁: 6.635e-10, C₂: 9.054e-10, C₃: 2.1e-10, C₄: 7.062-10, C₅: 4.169e-10, L₁ : 6.317e-10, L₂: 3.615e-10.
This values are divided by GM of the GM-cell

## Slide 25: Impelementation: Specs
NF = 12dB → integrated output noise = 99uV
IIP3dBV = IIP3dBm – 10 = 6dBV (peak)
IP2dBV = 45dBV

## Slide 26: Proposed GM-cell: (Two stages)
Notes : VDD = 1.6V ,Current mirrors and common mode feed back isn’t done yet

## Slide 27: Filter intial results:
Frequency response: shows peaking at 240MHz

## Slide 28: Filter intial results: (cont.)
Peaking is probably caused by this stage,because it has no external capacitors

## Slide 29: Filter results :Temporary solution
Adding Passive RC section before the filter, can reduce this peaking
Also can serve as the other mode of the filter (3dB BW=600MHz)
But it produces noise and losses
Also it’s very sensitive to parasitics

## Slide 30: Filter results after RC-section:
Peaking is reduced but losses increase, achieved output noise = 96uV

## Slide 31: Filter Schematic and Test bench

## Slide 32: Filter Results summary (till now):
Output noise= 96uV (NF =11.7dB) < 99u
Power Consumption = 100.8mA*1.6 = 161.28mW
OIP3 = -11dBV (Problem)

## Slide 33: Linearity Problem
Internal node of the filter shows larger peaking,which degrades linearity
Also for the second stage of the GM-cell the swing is limited (maybe using PMOS as input pair is better here)

## Slide 34: What’s to be done
Modify GM-cell to achieve IP3 spec and to eliminate peaking
CM and CMFB implementation
Getting all the results across corners: BW,GD,NF,IP3 and IP2
Starting Layout